## Slide 1
1. Hardware Reception: the network interface card (NIC) receives the frame on the wire. D epending on its driver configuration, the NIC transfers the frame either to an internal hardware buffer memory or to a specified ring buffer.
2. Hard IRQ: the NIC asserts the presence of a net frame by interrupting the CPU. This causes the NIC driver to acknowledge the interrupt and schedule the soft IRQ operation.
3. Soft IRQ: this stage implements the actual frame-receiving process, and is run in softirq context. This means that the stage pre-empts all applications running on the specified CPU, but still allows hard IRQs to be asserted. In this context (running on the same CPU as hard IRQ, thereby minimizing locking overhead), the kernel actually removes the frame from the NIC hardware buffers and processes it through the network stack. From there, the frame is either forwarded, discarded, or passed to a target listening socket. When passed to a socket, the frame is appended to the application that owns the socket. This process is done iteratively until the NIC hardware buffer runs out of frames, or until the device weight (dev_wei ht). For more information about device weight, refer to Section 8.4.1, “ NIC Hardware Buffer”
4. Application receive: the application receives the frame and dequeues it from any owned sockets via the standard POSIX calls (read , recv, recvfro m). At this point, data received over the network no longer exists on the network stack.
Resources:
Red_Hat_Enterprise_Linux-6-Performance_Tuning_Guide-en-US.pdf
Red_Hat_Enterprise_Linux_Network_Performance_Tuning_Guide.pdf
https://www.coverfire.com/articles/queueing-in-the-linux-network-stack/
https://community.mellanox.com/docs/DOC-1481
https://blog.packagecloud.io/eng/2017/02/06/monitoring-tuning-linux-networking-stack-sending-data/
NIC Ring Buffer
HardIRQ
Socket Queue (aka Qdisc;)
SoftIRQ
File Descriptor’s Buffer
DATA
DATA
NIC FIRMWARE
KERNEL
User Space
CPU

## Slide 2
NIC Ring Buffer
HardIRQ
File Descriptor’s Socket Queue (aka Qdisc;)
SoftIRQ
App Buffer
DATA
DATA
NIC FIRMWARE
KERNEL
User Space
CPU
CONFIGURATION FILE:
/etc/sysctl.conf
/proc/sys/net/core/default_qdisc
Qdisc=Pfifo_fast: deep queue and not flow aware
/proc/sys/net/core/dev_weight
The max number of frames the NIC can receive before the SoftIRQ triggers CPU to empty the Qdisc (decrease to speedup the Qdisck emptying by CPU).
/proc/sys/net/core/netdev_budget
The duration of the SoftIRQ in CPU time (For high speed NICs, increase so the CPU has more time to empty the Qdisc). Increase the budget if any of the columns besides the 1st one are increasing in /proc/net/softnet_stat
watch –d –n 0.5 ‘cat /proc/net/softnet_stat’
/proc/sys/net/core/netdev_max_backlog
Sets the maximum number of packets allowed to queue when a particular interface (NIC) receives packets faster than the kernel can process them.
/proc/sys/net/core/optmem_max
Configures the maximum ancillary buffer size allowed per socket
Socket Receive Buffer Size in bytes. Crank up these values to increase the queue depth to avoid Buffer overruns:
/proc/sys/net/core/rmem_default
/proc/sys/net/core/rmem_max
/proc/sys/net/core/wmem_default
/proc/sys/net/core/wmem_max
TO DEBUG, USE:
watch –d –n 0.5 ‘cat /proc/net/snmp’
an increase in UDP input errors indicates that one or more socket receive queues are full when the network stack attempts to queue new frames into an application's socket.
Make sure interrupts are well balanced across CPU cores:
watch –d –n 0.5 ‘cat /proc/interrupts’
watch –d –n 0.5 ‘netstat –su’ #statisticsUdp
watch -d -n 0.3 'netstat –neopau’ #numericExtendedTimersProgramAllUdp
Recv-Q the count of bytes yet to be copied by the user’s application from the buffer.
Send-Q the count of bytes yet to be acknowledged by the remote host.
dropwatch –l kas -> start
Monitors the packets that are dropped by KERNEL
echo ‘MTU=9000’ >> /etc/sysconfig/network-scripts/ifcfg-ethN
ethtool –g|G eth4 tx|rx-jumbo|rx-mini|rx N
Show/Set Ring Buffer depth.
ethtool –l|L eth4 tx|rx N
Show/Set Ring Buffer Channels. Where a channel is a set of queues with a single IRQ.
ethtool –a|A eth4 rx|tx on
Configure Flow Control on the NIC to send PAUSE frames to the switch.
ethtool -c|C eth4 adaptive-rx off rx-usec 0 rx_frames 0
Configures Interrupt Coalescence: the amount of traffic that NIC must receive, or time passed after receiving traffic before issuing a Hard Interrupt.
ethtool –k|K eth4
NIC Offloads should be used on high speed systems that transmit or receive large amounts of data and favor throughput over latency.
watch -d -n 0.5 'ethtool -S eth4 | grep \
"cleaned\|misses\|dropped\|error\|failed\|stopped\|\
flushed\|aggregated\|errors\|collisions\|timeout\|offload\|desc\|filtered\|jabbers"'
To avoid Qdisc overruns: in your program, increase the rate at which the recv() or read() calls are performed to empty the Qdisc more rapidly.
CPU Performance:
x86_energy_perf_policy –r
x86_energy_perf_policy performance
numactl --physcpubind=10,11,12,13 --membind=0
CPU Monitoring:
turbostat -interval 1 --debug
watch -d -n 0.5 numastat -n
numa_miss #BAD if incrementing
numa_foreign #BAD if incrementing
watch -d -n 0.5 numastat -m

## Slide 3
/etc/sysctl.conf
/etc/sysctl.d
sysctl –system|-p
Files:
/proc/interrupts #lists SoftIRQs per Qdisc
/proc/meminfo
/proc/mounts
/proc/partitions
Directories:
/proc/filesystems
/proc/sys
/proc/net/snmp #application queue
/proc/net/dev
/proc/net/tcp
/proc/net/unix
/proc/net/bonding/bondN
/proc/sys/net/core/dev_weight
/proc/sys/net/core/netdev_budget
/proc/sys/net/core/rmem_default
/proc/sys/net/core/rmem_max
/proc/sys/net/core/wmem_default
/proc/sys/net/core/wmem_max
/proc/sys/net/core/default_qdisc
/proc/ide/ replaced by sysfs
/proc/pci replaced by lspci –v (use lspci –v | grep –A 18 Mellanox for mellanox)
/proc/softirqs
watch -d -n 0.5 'ethtool -S eth4 | grep cleaned\|misses\|dropped\|error\|failed\|stopped\|flushed\|aggregated\|errors\|collisions\|timeout\|offload\|desc\|filtered\|jabbers"'
dropwatch -> start
watch -d -n 0.5 'netstat -su'
watch -d -n 0.5 'cat /proc/net/snmp'

## Slide 4
Bottle neck reasons:
IRQs are not balanced correctly (see if interrupts are spread across multiple CPUs: /proc/interrupts)
Socket Buffer Queue overflow:
  SoftIRQ misses: Insufficients netdev_budget (only the first column should have the counters incrementing, the rest of the columns must be zeroed)
  Insufficient CPU time allocated per IRQ (see CPU runtime using top command, see netstat –su for UDP errors, and see 2 above).
3. NIC Ring Buffer is too deep (Qdisk is too shallow)
4. NIC Interrupt Coalescence is insufficient

## Slide 5
sysctl is used to modify kernel parameters at runtime. The parameters available are those listed under /proc/sys/
variable
The name of a key to read from. An example is kernel.ostype. The ’/’ separator is also accepted in place of a ’.’.
variable=value
To set a key, use the form variable=value, where variable is the key and value is the value to set it to. If the value contains quotes or characters which are parsed by the shell, you may need to enclose the value in double quotes. This requires the -w parameter to use.
-n Use this option to disable printing of the key name when printing values.
-e Use this option to ignore errors about unknown keys.
-N Use this option to only print the names. It may be useful with shells that have programmable completion.
-q Use this option to not display the values set to stdout.
-w Use this option when you want to change a sysctl setting.
-p Load in sysctl settings from the file(s) specified or /etc/sysctl.conf if none given. Specifying - as filename means reading data from standard input.
--system
Load settings from all system configuration files.
/run/sysctl.d/*.conf
/etc/sysctl.d/*.conf
/usr/local/lib/sysctl.d/*.conf
/usr/lib/sysctl.d/*.conf
/lib/sysctl.d/*.conf
/etc/sysctl.conf
-a Display all values currently available.
-A Same as -a
EXAMPLES
/sbin/sysctl -a
/sbin/sysctl -n kernel.hostname
/sbin/sysctl -w kernel.domainname="example.com"
/sbin/sysctl -p /etc/sysctl.conf
NOTES
Please note that modules loaded after sysctl is run may override the settings (example: sunrpc.* settings are overridden when the sunrpc module is loaded). This may cause some confusion during boot when the settings in sysctl.conf may be overriden. To prevent such a situation, sysctl must be run after the particular module is loaded (e.g., from /etc/rc.d/rc.local or by using the install directive in modprobe.conf)
FILES
/proc/sys /etc/sysctl.conf
SEE ALSO
sysctl.conf(5), modprobe.conf(5)